## Slide 1: NetEngine 8000 X Series All Scenarios Intelligent Routers
The NetEngine 8000 X series are full-service intelligent metro routers launched by Huawei to meet the requirements of new services and massive connections in the cloud era. The X series adopts a hardware architecture with provides a capacity of 1T per slot and it could be upgrade from 1T per slot to 19.2T per slot, and also supports SRv6 for end-to-end intelligent connections, and integrates AI-boosted intelligent O&M capabilities, helping carriers build simplified intelligent metro networks. The X series applies to metro core, aggregation, DC gateway, and international gateway scenarios.
1
Overview
NetEngine 8000 X4 Router
NetEngine 8000 X8 Router
NetEngine 8000 X16 Router
Product Highlights
Highlights | Description
Super Capacity | Large Capacity : 19.2T/slot, twice the industry average High density board : 6*800GE, 36*400GE, 40*100GE, 72*25GE/10GE Orthogonal architecture, saving 24% space
Various Ports | Support P/PE, SR, IGW, DC-GW and BNG 800GE/400GE/100GE/50GE/40GE/25GE/10GE/GE/FE Support Integrated Line Processing Unit and Flexible card
All Scenarios | Metro core, Metro aggregation, DC-GW, SR scenarios, BNG, CGN, IPSEC, SA etc.
Product Appearance
Huawei NetEngine 8000 X series products include NetEngine 8000 X4, NetEngine 8000 X8, and NetEngine 8000 X16.

## Slide 2
2
Application Scenarios
The NetEngine 8000 X series are large-capacity, highly reliable, and energy-saving routers developed by Huawei to meet the interconnection requirements of the cloud and AI era. The NetEngine 8000 X series routers can be deployed in the following positions: PE/P, Metro aggregation, Metro core, DC-GW, and IGW.
BNG
Metro
Metro Fabric
IP Core
P&PE
P&PE
PE&IGW
IGW
PE&IGW
Internet
IXP
Public
P&PE
Telco Cloud
DC-GW
4
1
3
5
2
Spine

## Slide 3
Product Features
Category | Product Features |  | 
Category | NetEngine 8000 X4 | NetEngine 8000 X8 | NetEngine 8000 X16
L2 | IEEE 802.1q, IEEE 802.1p, IEEE 802.3ah, IEEE 802.1ag, STP/RSTP/MSTP, G.8032, LACP, VxLAN, VLAN and bridge domain |  | 
L3 | OSPF, OSPFv3, RIP, RIPng, IS-IS, IS-ISv6, BGP, BGP4+, ACL, ACL6, 6PE, 6VPE, Static routes, GRE, |  | 
MPLS | LDP, RSVP-TE, VPLS, VPWS, L3VPN, Seamless MPLS |  | 
SR MPLS | ISIS/OSPF/BGP for SR MPLS, SR MPLS BE, SR MPLS TE, SR MPLS TE Policy, SR-MPLS Flex-Algo, TI-LFA, Anycast FRR, SR-MPLS Microloop Avoidance, SR-MPLS OAM |  | 
SRv6 | ISIS/OSPFv3/BGP for SRv6, SRv6 BE, SRv6 policy, SRv6 Flex-Algo, BGP Policy, SRv6 SRH Compression, SRv6 TI-LFA FRR, Anycast FRR, SRv6 Microloop Avoidance, SRv6 OAM, SRv6 SFC, APN6 |  | 
EVPN | EVPN L3VPN, EVPN VPWS, EVPN VPLS |  | 
Multicast | IGMP, MLD, Static Multicast Routing, PIM-SM/SSM, MSDP, MBGP, Rosen MVPN, MVPN, NG MVPN, Multicast NAT, BIER, BIERv6 |  | 
Slicing | FlexE, Channelized Sub-interface, Slice-ID |  | 
QoS | 5 Level HQoS |  | 
Clock | 1588v2, Synchronous Ethernet Clock, G.8275.1, G.8275.2, SMPTE-2059 |  | 
OAM | IFIT, Telemetry, NetStream, SNMP, NQA, TWAMP, RFC2544, Y.1564, BFD, SBFD, MPLS OAM, MPLS TP OAM, VRRP, Ethernet OAM, Y.1731 |  | 
BNG | PPPoE, IPoE, L2TP , 802.1x, EDSG |  | 
Value add services | CGN, IPSEC, SA |  | 
4

## Slide 4
Product Specifications
Category | Specification |  | 
 | NE8000 X4 | NE8000 X8 | NE8000 X16
Slot Capability | 1T/2T/4T/9.6T/14.4T/19.2T per slot | 1T/2T/4T/9.6T/14.4T/19.2T per slot | 1T/2T/9.6T/14.4T per slot
Service slots | 4 | 8 | 16
Dimensions (WxDxH, mm) | 442 x 872 x 437.4 (9.8U) | 442 x 872 x 703 (15.8U) | 442 x 1033 x 1436 (32.3U)
Chassis height [U] | 9.8 U | 15.8 U | 32.3 U
Weight without packaging [kg(lb)] | 72 kg (158.7 lb) | 94 kg (207.2 lb) | 244.8 kg (539.69 lb)
Weight with packaging [kg(lb)] | 138 kg (304.2 lb) | 177 kg (390.2 lb) | 315.6 kg (695.78 lb)
Weight without packaging (full configuration) [kg(lb)] | 4T bundle：192.7 kg (424.8 lb); 14.4T bundle：210.1 kg (463.2 lb) | 4T bundle: 308.5 kg (680.1 lb); 14.4T bundle: 340.5kg (750.7 lb) | [ LPUI-4T boards are fully configured]: 666.1 kg ( 1468.5 lb); [LPUI-14.4T boards are fully configured]: 707.7 kg ( 1558.9 lb)
Typical power consumption (with configuration) [W] | 5240 W (estimated value when LPUI-4T boards are fully configured); 8860 W (LPUI-14.4T boards are fully configured) | 10256 W (estimated value when LPUI-4T boards are fully configured) | 24015 W (estimated value when LPUI-4T boards are fully configured); [LPUI-14.4T boards are fully configured]: 35965 W
Typical heat dissipation (with configuration) [BTU/hour] | 17324 BTU/hour | 32665 BTU/hour | [LPUI-4T boards are fully configured]: 77913 BTU/hour; [estimated value when LPUI-14.4T boards are fully configured]: 116684 BTU/hour
MTBF [year] | 18.71 year | 18.61 year | 18.53 year
MTTR [hour] | 0.5 hour | 0.5 hour | 0.5 hour
Availability | 0.99999 | 0.99999 | 0.99999
Power supply mode | DC/AC/HVDC built-in | DC/AC/HVDC built-in | DC/AC/HVDC built-in
Maximum number of power chassis inputs | (12 channels/PEM)*1 PEM=(2 channel/PM)*6 PM*1 PEM=12 channels | (20 channels/PEM)*1 PEM=(2 channels/PM)*10 PM*1 PEM=20 channels | (40 channels/PEM) x 1 PEM = (2 channels/PM) x 20 PMs x 1 PEM = 40 channels
3

## Slide 5
Product Specifications
3
Category | Specification |  | 
 | NE8000 X4 | NE8000 X8 | NE8000 X16
Rated input voltage [V] | DC: -48/-60 V; AC: 200 V to 240 V; HVDC: 240 V/380 V |  | 
Input voltage range [V] | DC: -40~-72V; AC: 176 V to 290 V; HVDC: 188 V to 400V |  | 
Maximum input current [A] | DC: 58.5 A/single-module; AC: 16 A per module; HVDC: 14 A per module |  | 
Maximum input cable size [mm²] | 2.5 mm² | 2.5 mm² | 2.5 mm²
Heat dissipation mode | Air cooling | air cooling | Air cooling
Airflow direction | Front-to-back airflow | Front-to-back airflow | Front-to-back
Number of slots | 14 | 18 | 24
Number of service board slots | 4 | 8 | 16
Switching capacity | 41.89 Tbit/s; 173.15 Tbit/s (14.4T bundle) | 83.78 Tbit/s;14.4T bundle：346.3 Tbit/s | 692.60 Tbit/s
Redundant MPUs | 1:01 | 1:01 | 1:01
Redundant Switch fabrics | 7+1/3+1 | 7+1/3+1 | 7+1/3+1
Redundant power supply | Max6，N+1 | Max10，N+1 | Max20，N+1
Redundant fans | 3 assemblies in support for proper fan operation in case of a single fan failure for a short period at 40°C (104°F) | 3 assemblies in support for proper fan operation in case of a single fan failure for a short period at 40°C (104°F) | Three module frames. The system can work for a short period of time when a single fan fails. (The operating temperature is 40°C.)
Long-term operating temperature [°C(°F)] | 0 °C to 40 °C (32°F to 104°F) |  | 
Short-term operating temperature [°C(°F)] | -5 °C to 50 °C (23°F to 122°F) |  | 
Restriction on the operating temperature variation rate [°C(°F)] | ≤ 30°C/hour (54°F/hour) |  | 
Storage temperature [°C(°F)] | -40 °C to 70 °C(–40°F to 158°F) |  | 
Long-term operating relative humidity [RH] | 5% to 85%, non-condensing |  | 
Short-term operating relative humidity [RH] | 5% to 95% RH, non-condensing |  | 
Storage relative humidity [RH] | 5% to 95% RH, non-condensing |  | 
Long-term operating altitude [m(ft.)] | <= 4000 m (13123.2 ft.) (For the altitude in the range of 1800 m to 4000 m [5905.44 ft. to 13123.2 ft.], the operating temperature of the NEU100 must decrease by 1°C [33.8°F] for every 220 m.) |  | 

## Slide 6
Support Boards
Category | Boards | Description
Integrated Line Processing Unit | LPUI-1T3 | 10*100GE QSFP28 MACsec + 36*10GE(SFP+)/GE(SFP) MACsec
 | LPUI-2T/ LPUI-2T-E/ LPUI-2T-L | 72*25GE(SFP28)/10GE(SFP+)/GE(SFP)
 |  | 20*100GE QSFP28
 |  | 20*100GE QSFP28 MACsec
 |  | 10*100GE QSFP28+36*25GE(SFP28)/10GE(SFP+)/GE(SFP)
 | LPUI-4T/ LPUI-4T-E/ LPUI-4T-L | 8*400GE QSFP-DD+8*100GE QSFP28
 |  | 4*400GE QSFP-DD+24*100GE QSFP28
 | LPUI-7T2 | 18*400GE QSFP-DD
 | LPUI-14T4 | 36*400GE QSFP-DD
 | LPUI-19T2 | 6 x 800GE QSFP-DD + 36 x 400GE QSFP-DD
Integrated Service Unit | / | VSUI-400-E + CGN/IPSEC/SA RTU MSUI-400-E + Data Redundancy Elimination RTU
Flexible Card | LPUF-1T/ LPUF-1T-E | P1T: 36*10GE SFP+; 1 x 400GE+1 x 100GE
 |  | P1T: 5*100GE QSFP28
 |  | P1T: 10*10GE + 16*155M/16*622M/8*2.5G/2*10G POS
 | LPUF-2T | P1T: 36*10GE SFP+
 |  | P1T: 5*100GE QSFP28
 |  | P2T: 10*100GE QSFP28
 |  | P2T: 2*400GE QSFP-DD+2*100GE QSFP28
 | LPUF-6T4 | 4 x 400GE QSFP-DD +16 x 100GE QSFP28; 8 x 400GE QSFP-DD ;24 x 100GE QSFP28
5

## Slide 7
More Information
For more information about the NetEngine 8000 X Series Routers, visit https://e.huawei.comor contact us in the following ways:
Global service hotline: http://e.huawei.com/en/service-hotline
Logging into the Huawei Enterprise technical support web: https://support.huawei.com/enterprise/
Sending an email to the customer service mailbox: support_e@huawei.com
Copyright © Huawei Technologies Co., Ltd. 2022. All rights reserved. No part of this document may be reproduced or transmitted in any form or by any means without prior written consent of Huawei Technologies Co., Ltd. Trademarks and Permissions and other Huawei trademarks are trademarks of Huawei Technologies Co., Ltd.. All other trademarks and trade names mentioned in this document are the property of their respective holders. Notice The purchased products, services and features are stipulated by the contract made between Huawei and the customer. All or part of the products, services and features described in this document may not be within the purchase scope or the usage scope. Unless otherwise specified in the contract, all statements, information, and recommendations in this document are provided "AS IS" without warranties, guarantees or representations of any kind, either express or implied. The information in this document is subject to change without notice. Every effort has been made in the preparation of this document to ensure accuracy of the contents, but all statements, information, and recommendations in this document do not constitute a warranty of any kind, express or implied. | Huawei Technologies Co., Ltd. Address:Huawei Industrial Base Bantian, Longgang Shenzhen People's Republic of China Postcode:518129 Website:www.huawei.com
6